## Slide 1: Living Shorelines in San Francisco Bay
Marilyn Latta
Project Manager
CA State Coastal Conservancy
Bay Area Flood Protection Agencies
Annual Meeting
Napa, CA
September 30, 2026
Notes: My name is Marilyn Latta, I’m a project manager with the State Coastal Conservancy and excited to present at the conference today. The Coastal Conservancy is a state agency that works with partners to protect and preserve CA’s coast and San Francisco Bay. We are a funder but we also help lead projects, especially when there is a need for a state agency to help coordinate across jurisdictions or advance challenging new project types to address regional issues such as sea level rise. The Conservancy has been championing Living Shorelines efforts since 2010, and we work with a wide variety of local, state, and federal partners to build capacity for living shorelines work in the state and in San Francisco Bay. I’ve had the great pleasure of working with a diverse set of dedicated partners in developing and implementing multi-habitat and multi-objective living shorelines pilot projects in San Francisco Bay over the last 14 years. Some of the primary key partners include San Francisco State University’s Estuary and Ocean Science Center, Smithsonian Environmental Research Center, UC Davis, USGS Western Ecological Research Center, Environmental Science Associates, The Nature Conservancy, and additional landowners and contractors.
I will share some key highlights from this work, including why our teams feel increased urgency to transfer knowledge and scale projects up faster through our new Regionally Advancing Living Shorelines Project.

## Slide 2: Many Definitions and Interpretations
Shoreline protection via strategic restoration design
Diverse suite of habitat approaches and methods
Minimize coastal erosion, maintain coastal processes
Natural habitat for plants, wildlife, and people
Sea level rise adaptation
Carbon sequestration
Notes: There are many different definitions for living shorelines, a term which originated on the east coast. Locally more work is needed to define the term for the west coast conditions and habitat types, in both sheltered estuaries and outer coast environments. The term specifically refers to strategically designing restoration treatments to achieve co-equal goals of biological habitat enhancement and physical shoreline protection. This can include a suite of techniques and habitat approaches at different tidal elevations, all designed to minimize coastal erosion, maintain coastal processes, and provide natural habitat for plants, fish and wildlife, and people. NOAA, Restore America’s Estuaries, the Army Corps Engineering with Nature Program, others have been strong leaders in this field.
Regionally, climate risk assessments by county are in process or have generally been completed, but specific adaptation plans and guidance on effective and sustainable nature-based adaptation methods haven’t been substantially developed. For many sites this requires new methods and design approaches that haven’t been tried locally before, and planners preparing adaptation strategies are hesitant to include innovative ideas that haven’t been tested or documented. But Living shorelines approaches provide an opportunity to better connect the less studied underwater nearshore habitats like shellfish reefs and eelgrass beds as a linked gradient with mudflats, beaches, marshes and other adjacent habitats up the slope.

## Slide 3
CA / SF Bay Policy and Regulatory Support
Vetted Regional Goals with Input from Many Stakeholders and Agencies
Recognition of nature-based adaptation and living shorelines– local, state, federal
Notes: 3
The Army Corps of Engineers approved Nationwide Permit 54 for living shorelines in 2017, but it has limited use locally- as projects have a cap of 500 linear feet and within 30 feet of the mean tide line. The corps can modify future regional conditions to better fit local project types.
We have supportive policies in CA that recommend further testing of living shorelines, and there has been concerted regional collaborative efforts to link habitats and restoration approaches. We have excellent guidance documents and the next step is to test specific designs on the ground, so we can learn what will work where and how best to scale up with the right mix of methods.

## Slide 4
Notes: In San Francisco Bay, many partners are working to connect multiple shoreline habitats up the shoreline slope, from the aquatic habitats that are hidden from sight to the upper edge that is adjacent to our communities. Each habitat plays an important role in the natural ecoysystem and climate adaptation. This connected habitat approach provides cumulative benefits for reducing wave energy and providing space for plants and animals to thrive.

## Slide 5
Example Pilot Projects in SF Bay 2012-2025
(Oyster Reefs, Eelgrass Beds, Tidal Marsh, Upland Ecotone, Creosote Removal)
SF Bay Living Shorelines Project: San Rafael (Olympia oysters, eelgrass)
(SCC, SF State, UC Davis, ESA, USGS)
SF Bay Living Shorelines Project: Giant Marsh (oysters, eelgrass, tidal marsh, upland ecotone)
(SCC, SF State, UC Davis, ESA, USGS, OEI)
SF Bay Creosote Removal: Red Rocks (piling and debris removal, oysters, eelgrass, rockweed)
(SCC, AECOM, Ducks Unlimited, Merkel)
Terminal 4 Wharf Removal (largest derelict wharf SF Bay, enhanced rock slope): (SCC, COWI, CSWst2, Merkel, TWNC)
Notes: Here is a map of several Living Shorelines efforts occurring in San Francisco Bay. I will share some design and implementation highlights from the State Coastal Conservancy’s first project in San Rafael, and with two additional projects that build on the lessons learned, and link in more habitats and activities.

## Slide 6: San Rafael Living Shoreline Project
Notes: This first case study is a project the Conservancy and 17 partners constructed in 2012, to test restoration techniques for oyster and eelgrass beds and the benefits of these habitats on shoreline protection. Main design and monitoring partners include ESA, SFSU, UC Davis, USGS, and the landowner The Nature Conservancy.

## Slide 7
Link to Subtidal Habitat Goals
Pilot scale, experimental approach
Monitor use by invertebrates, fish, birds
Assess interactive effects of oysters + eelgrass
Evaluate physical benefits
Pilot climate change adaptation
Apply lessons learned to future projects
Multiple habitats & objectives
Photos, S. Kiriakopolos
Notes: This project has multiples objectives, including:
Implementing recommendations in Subtidal Habitat Goals Report
Using a pilot scale, experimental approach that built upon past, successful trials of restoration of eelgrass and native oyster habitats separately
Monitoring wildlife use to demonstrate habitat values
Assessing the interactions of oysters and eelgrass when restored together
Evaluating the physical benefits including wave energy reduction and sediment accretion
We considered how these activities might contribute to climate change adaptation strategies
And we are applying lessons learned from this pilot project to future projects in the Bay and across the state

## Slide 8
Existing Uses
Parcel Ownership
Bathymetry
Depths for Habitat Restoration
Depths for Access
Orientation to Wind/Waves
Existing Species and Habitats
Sea Level Rise Modeling
Physical Space Required
Site Specific Considerations
Notes: There are many site specific considerations we had to carefully evaluate, including..
In our estuary, you can see the map of bathymetry which informs where oyster/eelgrass projects would be appropriate. But then the lower right map shows parcel ownership, with public in yellow and private in red. It’s critical to identify the landowners and make sure they are supportive of the project.
It’s important to do strong desktop planning and also extremely important not to stay focused on paper planning for too long- make sure to get out to the project site with potential partners, look at existing conditions at different tides and times of year, and talk about constraints and opportunities for design, construction access, and monitoring access.

## Slide 9
Notes: Two sites in our current project.
TNC property in San Rafael,
And a location in Hayward just south of the San Mateo bridge and adjacent to the ELER

## Slide 10: Construction Prep: “Baycrete” Reef Balls, Layer Cakes, Oyster Blocks
Photos, M. Latta
Notes: Here is the fabrication process for the reef ball and other hybrid elements. Because no contractor had ever done this before in the San Francisco Bay Area, the Conservancy and partners brought in a contractor from Reef Innovations in Sarasota FL to lend their experience and oversee the effort, although they had never worked with Baycrete. They worked alongside local contractor Dixon Marine Services. We really appreciate everyone’s willingness to experiment together and try new things- as we are truly in a research and development phase with this work here locally.

## Slide 11: Construction July- August 2012
Notes: These are a few pictures of the construction in July/August 2012- starting with oyster element placement by barge, which occurred at specific tide windows deep enough to allow boat access but shallow enough to allow placement assisted by people in the water. Eelgrass plantings came after the construction of the harder elements.

## Slide 12
Photos, S. Kiriakopolos
Intensive Monitoring 2012-2017
Eelgrass and Oyster success
Invertebrates- benthic and on reef
Fish- acoustic, traps, seining
Birds- shorebirds and waterfowl
Physical-
  bathymetry
  sediment accretion and erosion
  reef elements
  water quality
  wave attenuation
Notes: Because subtidal restoration work in general is at its early stages in our estuary, as well as living shorelines, it is critical to carefully monitor the species response and the ecosystem functions and services that are gained from the project. We don’t have published data or even grey literature on these topics, so this project was designed with heavy monitoring to provide some of the first data on benefits and success. This included intensive quarterly sampling events, often at extreme low tides, and a lot of coordination between groups so that we didn’t have conflicts between activities.

## Slide 13
Photos, S. Kiriakopolos, Damien Kunz, and Sally Rae Kimmel
3.8 Million Native Oysters and 100 Species Using Reefs
Physical Benefits
most energy lost on broad mudflat
but reef extracts 30% more at MSL water levels
15 cm sediment
accretion along reefs
24 cm in center
Notes: We’ve seen a huge increase in the number of taxa and species using the site, compared to when it was an unstructured mudflat. These include Dungeness crabs, red rock crab, nudibranchs, great egrets, american black oystercatchers, and many other species.
We’ve also documented physical benefits- including sediment accretion both along and within the reef structures, and a 30% increase in wave attenuation compared to the mudflat alone.

## Slide 14
Recommendations for future projects
Add habitat structure on mudflat to quickly attract many species, including rare & valuable
Plant eelgrass early in the growing season, plan for additional phased plantings
Co-locate eelgrass and oyster reefs to maximize invertebrate/fish use
Shell bag mounds and baycrete elements maximize native oyster recruitment
Consider accretion around reefs in future designs – don’t waste valuable shell at base
Don’t fret about reef subsidence, even in unconsolidated sediment
Test more locations, additional designs, to further evaluate wave attenuation potential
Add in additional habitat types – tidal marsh edge, seaweeds, beaches
Test in combination with creosote piling removal and rocky intertidal shoreline elements

## Slide 15
Giant Marsh Living Shorelines Project 2019-2024
High Marsh/ Ecotone
High Tide Refugia
Tidal marsh habitat
Endangered Species
Oysters, Eelgrass, Rockweed, Pacific Cordgrass, CA Seablite, Upland Ecotone
Notes: The Giant Marsh Living Shorelines Project design was completed in Fall 2016 and includes 7 different habitat treatments, that range from oyster reef and eelgrass plantings, seaweed treatments, and tidal marsh and upland ecotone components. There are 3 different oyster reefs in the design, each paired with a different vegetative component- eelgrass, Pacific rockweed, and Pacific cordgrass. They are sited at different tidal heights and shoreline orientations, and different reef types and materials. The CA eelgrass, rockweed, and seablight plantings were installed in 2019, and the Pacific cordgrass and upland ecotone plantings are planned for next winter 2021-22.

## Slide 16
Pacific herring substrate
Eelgrass Beds- main focus
Oyster Reefs- protection
Rockweed- experimental
Creosote/ Debris Removal
Key Step Living Shorelines
Notes: The Coastal Conservancy partnered with National Fish and Wildlife Foundation to assess sites baywide for the best opportunities to match creosote removal with living shorelines and a focus on Pacific herring. We removed more than 420 tons of debris and 460 pilings from the old Red Rocks Warehouse at site in the City of Richmond. This work removes toxic fill and allows more space for living habitat. The restoration phase occurred in Summer 2018, and includes shell bag mounds, Reef balls, eelgrass plantings, and rockweed relocation.

## Slide 18: Crown Plantings, Seaweed Cobbles, Oyster Reefs

## Slide 19: Constructability in Different Settings
Importance of Assessing Feasibility
Basic Site Suitability and Access
Supportive Environmental Factors
Stressors and Adjacent Land Uses
Land Ownership and Preferences
Sensitive Habitats and Permit Req’s
Opportunities to Field Test Methods
Refine Methods Across Elevations
Terrestrial and Marine Equipment
Small and Large scale treatments
Seasonal Phasing of Activities
Document & Share Challenges/Solutions
Notes: Constructability considerations vary considerably in different settings.
It’s important to carefully assess site and habitat suitability before going too far down the design path. This includes assessing supportive environmental factors (bottom type, water quality, habitat conditions) as well as stressors and adjacent land use. If it’s a project that starts initially without landowner involvement, it’s important to identify land ownership and gain permission from the landowner early on in project design, as it can influence design, siting, specific permitting and contracting procedures, and ultimately they need to be a permit applicant and it’s critical to whether the project will move forward.
Living Shorelines Projects provide opportunities to refine methods across elevations, refine best equipment approaches with using combinations of terrestrial and marine equipment, test phasing or combinations of small and large scale treatments, seasonal phasing of activities, and documenting and sharing best techniques so that the next project doesn’t have to start from scratch.

## Slide 20
Green Jobs and Job Training
Notes: The project also includes future workforce development trainings led by SFSU Estuary and Ocean Science Center, Smithsonian, and other partners who will work with local Conservation Corps and other community organizations. These field trainings will provide opportunities for local youth and adults to gain skills in tasks involved in different methods and green grey materials- such as collecting eelgrass, propagating and outplanting native vegetation, and using clean pacific oyster half shell and other hybrid green grey methods to build reefs. All of this experimentation provides jobs and helps better connect Bay Area communities to gain skills and get engaged in the green restoration economy.

## Slide 21
Collaborative Partnerships
People, Technology, and Science
Notes: It’s been important to develop Collaborative Partnerships to implement this work- one agency can’t do it alone and any project is stronger with partners. We are assembling diverse interdisciplinary teams that approach our shared goals via different skills and strengths; and working together on designs that integrate biology and engineering. The projects are stronger and more connected to the community because of the mix of university researchers and graduate students, consulting firms, non-profits, and marine contractors, all working with local, state and federal agencies to innovate and achieve a common goal.

## Slide 22
Regionally Advancing Living Shorelines
Coalition Approach:
COLLABORATE
DESIGN ACROSS REGIONS
SCALE UP & BUILD ADAPTATION FASTER
TRANSFER AND SHARE KNOWLEDGE
Tasks:
Pilot Site Results, Baseline Data Collection
Regional Design/Constructability Guidance
Develop 30-60% Designs at 10 New Sites
Programmatic Permit Approach
Living Shorelines Collaborative Forum
Local Engagement/ Workforce Trainings
Notes: The Regionally Advancing Living Shorelines Project is a concerted effort to collaborate, design across regions, scale up and build adaptation faster, and transfer and share knowledge.
The project is led by the Coastal Conservancy and San Francisco Estuary Institute, with a coalition of key partners in the Central Bay, including Ducks Unlimited, Marin and Golden Gate Audubon Societies, East Bay Regional Park District, Port of San Francisco, and additional landowners and living shorelines practitioners that include agencies, non-profits, academic institutions, and consultants.
A key goal of this project is to work collaboratively with ten landowners in the Central Bay to design across regions and scale up and increase the pace and effectiveness of new living shoreline projects. We want to continue to increase our reach and the uptake of this work, by sharing our knowledge and lessons learned broadly, and directly apply them to new local demonstration projects to continue building this body of work and realize more substantial restoration outcomes.
The first phase is from 2023-2025 and is a $6.5M planning effort, funds have been secured from SFBRA, SCC, NFWF, and EPA.
The tasks include conducting pilot and baseline site data collection, developing regional design and constructability guidance, developing designs for 10 new ls sites, developing a programmatic permit approach that better outlines criteria and requirements for projects ahead of time, establishing a Living Shorelines Collaborative to share information, and hosting workforce develop trainings and field trips. The Collaborative forum will allow the sharing of technical information, discuss design and permitting issues, identify opportunities to leverage synergies, and foster a stronger community of living shoreline partners.
The 2nd phase is to construct the 10 new sites in 2026-2028, which we anticipate needing to raise at least $30M for with landowning site partners.

## Slide 23
Marilyn Latta, Project Manager
CA State Coastal Conservancy
marilyn.latta@scc.ca.gov
510-286-4157
Thank You
Questions and Discussion
Notes: Thanks so much to our partners and collaborators, especially to the SF Bay Restoration Authority, EPA SF Bay Water Quality Improvement Program, National Fish and Wildlife Foundation National Climate Resilience Fund, and State Coastal Conservancy sea level rise funds.